## Slide 1
Previous Lecture
organisational aspects
What is hydrogeology?
groundwater as part of the global water cycle
volume and mass budgets
Questions?

## Slide 2
Today
structure of the subsurface
grain size distribution of unconsolidated porous media
subterranean water
* The lecture texts/contents are originally from Prof. R. Liedl. Only minimal modifications have been made to the original texts/contents.

## Slide 3
Structure of the Subsurface

## Slide 4
Porous Medium
A porous medium or a porous body is a solid containing voids (or holes).
The subsurface can be regarded a porous medium.
Voids may have very different shapes (interstitial between ball-like grains, planar crack-like fractures, cylindrically shaped tubes or conduits etc.)
Voids may be connected to or disconnected from each other.
Voids may contain fluids (mostly air and/or water).
Size, shape and connectivity of voids are influential for the ability of the porous medium – to store water – to transmit water

## Slide 5
Types of Porous Media in the Subsurface
unconsolidated
porous medium
(formation due to deposition of solid
material mostly
by water)
consolidated
porous medium
(formation of rocks due to
increased pressure acting
together with thermal
and chemical processes)
fractured
karstified
sediments
rocks

## Slide 6
Unconsolidated Porous Medium
sediments consisting of fluvial deposits of sands and gravels
(Rhine Basin – Southwest Germany/Northern Switzerland)
(Klingbeil, 1998)

## Slide 7
Consolidated Porous Media
Fractured porous medium: Genesis of fractures or cracks due to mechanical or thermal processes (stress/strain or cooling/warming)
34 cm
Sandstone
(South Germany)
Gypsum
(Western Ukraine)
Karstified porous medium: Genesis of fractures or tubes (conduits) due to chemical processes (i.e. dissolution of rock by water)

## Slide 8
Porosity
Porosity (or more precise: total porosity) is defined as the volumetric share of voids in a porous medium:
Total porosities can be given either as numbers between 0 and 1 or as percentages between 0% and 100%.
void volume [L³]
total volume [L³]
total porosity [-]
Sponge
https://energyeducation.ca/encyclopedia/Porosity
Sourdough bread
Rye bread
https://en.wikipedia.org/wiki/Pore_(bread)

## Slide 9
Total Porosity of Artificial Porous Media
If „grains“ have identical shape and are regularly arranged, it is possible to exactly compute total porosity, e.g. for packed spheres of same size.
“dense packing“
“loose packing“
Figure Source: https://doi.org/10.1007/978-3-030-28140-3_2
Exact computation of porosity is not possible

## Slide 10
Total Porosity of Natural (Unconsolidated) Porous Media
In general, well sorted unconsolidated porous media exhibit larger total porosities than poorly sorted unconsolidated porous media (in the above example: 32% vs. 17%)
“well sorted“
(= grain diameters cover a small range)
“poorly sorted“
(= grain diameters cover a large range)
Natural unconsolidated porous media consist of grains of different size.
Total porosity depends on the grain size distribution.

## Slide 11
Typical Porosity Values
 | total porosity (%)
siltstone | 21 – 41
sandstone | 5 – 30
basalt | 3 – 35
claystone | 1 – 10
limestone | 1 – 10
shale | < 10
granite | < 1
 | grain diameter (mm) | total porosity (%)
coarse gravel | 20 – 60 | 24 – 36
fine gravel | 2 – 6 | 25 – 38
coarse sand | 0.6 – 2 | 31 – 46
fine sand | 0.06 – 0.2 | 26 – 53
silt | 0.002 – 0.06 | 34 – 61
clay | < 0.002 | 34 – 60
Total porosity of consolidated porous media (rocks) is usually smaller than total porosity of unconsolidated porous media. However, weathering effects may lead to increased values.
For unconsolidated porous media, total porosity tends to increase with decreasing grain size.
unconsolidated porous media
consolidated porous media

## Slide 12
Grain Size Distribution of Unconsolidated Porous Media

## Slide 13
Introductory Remarks
The ability of unconsolidated porous media to transmit water is highly dependent on the grain size distribution.
The grain size distribution is therefore frequently determined in laboratory experiments in order to deduce important flow properties.
There are five major grain size classes (ordered by increasing diameter): clay, silt, sand, gravel, cobbles (or debris)
The classes for silt, sand and gravel are usually subdivided by “fine“, “medium“, and “coarse“ (or “very fine“, “fine“, “medium“, „coarse“, and “very coarse“).
Different ranges for individual grain size classes have been defined by different authorities or regulators!
The standard method to determine the grain size distribution of a sample is sieve analysis.

## Slide 14
Classification Schemes
The diagram below includes a couple of classification schemes to define ranges of grain diameters for clay, silt, sand, and gravel.

## Slide 15
Sieve Analysis
Sample consists of different grain size fractions
grain diameter (mm)
cumulative mass fraction (%)
granulometric curve

## Slide 16
Sieving Machine

## Slide 17
Result
(diameters in mm)
< 0.063
6.3
4.0
2.0
1.0
0.63
0.4
0.2
0.15
0.063

## Slide 18
dx and U
dx denotes the grain diameter for which x % (in mass or weight, not volume!) of the sieved material is smaller than this diameter.
x
dx
Grain diameters d10, d60 and d75 are of practical importance with regard to groundwater flow properties.
The ratio of d60 and d10 is called coefficient of uniformity U :
d75 is specifically used for well construction purpo-ses (not covered by this lecture).
grain diameter (mm)
cumulative mass fraction (%)

## Slide 19
Example: Sieve Analysis
silt
sand
gravel
de-
bris
sieve analysis

## Slide 20
Subterranean Water

## Slide 21
The Subsurface as a Three-Phase System
In general, voids in the subsurface are partly occupied by air and water.
The subsurface can therefore be seen as a three-phase system consisting of a solid phase, a water phase, and a gas phase.
A schematic illustration for voids or pores in an unconsolidated porous medium is given in the figure.

## Slide 22
Some More Volume Ratios
The (volumetric) water content is defined as the share of water in the porous medium:
water volume [L³]
total volume [L³]
water content [-]
The water content cannot exceed total porosity, i.e.  ≤ n.
The degree of saturation is given by the ratio of water volume to void volume:
water volume [L³]
void volume [L³]
degree of saturation [-]
The degree of saturation S equals /n.
S may vary between 0 and 1 (or between 0% and 100%).
S = 0: no water in the voids; S = 1: voids are completely filled with water
Notes: n = Vv/Vt – some voids may be filled with air and so n is always bigger as it accounts for both water and aid voids.

## Slide 23
Forces Acting on Subterranean Water
Subterranean water is subject to several forces.
Most important are: – gravity – attractive forces between water molecules (cohesion) – attractive forces between water and solids (adhesion, see figure).

## Slide 24
Surface Tension
Cohesive forces acting on a water molecule compensate each other if the molecule is not located near the water-air or water-solid interface.
This is no longer true at an in-terface: cohesive interaction is reduced on one side. The resulting force tends to minimise the interface area.
Macroscopically, this effect is parametrised by the surface tension, which is defined as the energy needed to increase the area of the interface by one unit.
Common units of the surface tension s are J/m² or N/m. (Its dimension is M/T².)
The surface tension of water is about 7.5·10-2 N/m at 10°C.
Notes: Water has among the highest surface tension among the liquid

## Slide 25
Capillary Action
Water is subject to capillary action when adhesion is stronger than cohesion.
The capillary rise of water in a tube depends on the surface tension and the tube radius.
The maximum(!) capillary rise is given by:
capillary rise [L]
surface tension
of water [M/T²]
density
of water
[M/L³]
tube
radius
[L]
acceleration
of gravity
[L/T²]

## Slide 26
Capillary Action in the Subsurface
Capillary action plays a dominant role in the subsurface.
The capillaries are given by the individual pore channels.
Pore channels in poorly sorted material may strongly differ in diameter, such that a certain variability in capillary rise is observed.
“perfectly sorted
material”
“natural
material”

## Slide 27: Quick check what we have understood?
Pls. scan the QR- code
or
click link the link: partici.fi/89145883